## Slide 1: Technical Infrastructure: Networking
INFO1380
Conestoga College

## Slide 2: Topic 13 – Wireless Networking

## Slide 3: SMS message BOT
Encapsulation
More Standards Based
Not so much PAN

## Slide 4: Characteristics of Wireless Transmission
Wireless networks (WLANs)
  Networks that transmit signals through the air via radio frequency (RF) waves
Wired and wireless signals share many similarities
  Use of the same Layer 3 and higher protocols
The nature of the atmosphere makes wireless transmission different from wired transmission
Notes: Characteristics of Wireless Transmission
Wireless networks (WLANs)
  Networks that transmit signals through the air via radio frequency (RF) waves
Wired and wireless signals share many similarities
  Use of the same Layer 3 and higher protocols
The nature of the atmosphere makes wireless transmission different from wired transmission

## Slide 5: The Wireless Spectrum
The wireless spectrum is a continuum of electromagnetic waves used for data/voice communication
  Arranged by frequencies
    Lowest to highest
  Spans 9 KHz and 300 GHz
Wireless services associated with one area
FCC oversees United States frequencies
ITU oversees international frequencies
  Air signals propagate across borders
Notes: The Wireless Spectrum
The wireless spectrum is a continuum of electromagnetic waves used for data/voice communication
  Arranged by frequencies
    Lowest to highest
  Spans 9 KHz and 300 GHz
Wireless services associated with one area
FCC oversees United States frequencies
ITU oversees international frequencies
  Air signals propagate across borders

## Slide 6: The Wireless Spectrum
Notes: The Wireless Spectrum

## Slide 7: Signal Propagation
Notes: Signal Propagation

## Slide 8: Frequency Ranges
2.4-GHz band (older)
  Frequency range: 2.4–2.4835 GHz
  11 unlicensed communications channels
  Susceptible to interference
Unlicensed: no FCC registration required
5-GHz band (newer)
  Frequency bands
    5.1 GHz, 5.3 GHz, 5.4 GHz, 5.8 GHz
  24 unlicensed bands, each 20 MHz wide
  Used by weather, military radar communications
Notes: Frequency Ranges
2.4-GHz band (older)
  Frequency range: 2.4–2.4835 GHz
  11 unlicensed communications channels
  Susceptible to interference
Unlicensed: no FCC registration required
5-GHz band (newer)
  Frequency bands
    5.1 GHz, 5.3 GHz, 5.4 GHz, 5.8 GHz
  24 unlicensed bands, each 20 MHz wide
  Used by weather, military radar communications

## Slide 9: Frequency Ranges
Notes: Frequency Ranges

## Slide 10: Wireless PAN
WPANs rarely exceed a few meters geographically and usually only contain a few personal devices
Three common wireless technologies used to connect PAN devices are:
  Bluetooth
  Infrared (IR)
  Near-field communication (NFC)
Notes: Wireless PAN
WPANs rarely exceed a few meters geographically and usually only contain a few personal devices
Three common wireless technologies used to connect PAN devices are:
  Bluetooth
  Infrared (IR)
  Near-field communication (NFC)

## Slide 11: Wireless PAN
Bluetooth
  Operates in the radio band of 2.4 GHz to 2.485 GHz
  Hops between frequencies within that band
    Called frequency hopping
  Requires close proximity to form a connection
  Before two Bluetooth devices can connect, they must be paired
  Bluejacking - a connection is used to send unsolicited data
  Bluesnarfing - a connection is used to download data without permission
NFC (Near-Field Communication)
  A form of radio communication that transfers data wirelessly over very short distances
  Signal can be transmitted one way by an NFC tag, or smart tag
    When employees need access to a secure area
  The NFC tag collects power from the smartphone or other device by magnetic induction
Notes: Wireless PAN
Bluetooth
  Operates in the radio band of 2.4 GHz to 2.485 GHz
  Hops between frequencies within that band
    Called frequency hopping
  Requires close proximity to form a connection
  Before two Bluetooth devices can connect, they must be paired
  Bluejacking - a connection is used to send unsolicited data
  Bluesnarfing - a connection is used to download data without permission

## Slide 12: Wireless PAN
Notes: Wireless PAN

## Slide 13: Bluetooth Beacon

## Slide 14: Chromecast – Why Wifi??????

## Slide 15: Wi-Fi WLAN (Wireless LAN) Architecture
Notes: Wi-Fi WLAN (Wireless LAN) Architecture

## Slide 16: 802.11 WLAN Standards
Wireless technology standards
  Most popular: developed by IEEE’s 802.11 committee
Notable Wi-Fi standards
  802.11b, 802.11a, 802.11g, 802.11n, 802.11ac
  All standards use half-duplex signaling
  Standards vary at the Physical layer
  802.11n and later modify the way frames are used at the MAC sublayer
Notes: 802.11 WLAN Standards
Wireless technology standards
  Most popular: developed by IEEE’s 802.11 committee
Notable Wi-Fi standards
  802.11b, 802.11a, 802.11g, 802.11n, 802.11ac
  All standards use half-duplex signaling
  Standards vary at the Physical layer
  802.11n and later modify the way frames are used at the MAC sublayer

## Slide 17: Access Method
802.11 MAC services
  Append 48-bit physical addresses to frame
    Identifies source and destination
Same physical addressing scheme
  Allows easy combination with other IEEE networks
Wireless devices
  Not designed to simultaneously transmit and receive
  Cannot prevent collisions
  Use different access method than Ethernet
Notes: Access Method
802.11 MAC services
  Append 48-bit physical addresses to frame
    Identifies source and destination
Same physical addressing scheme
  Allows easy combination with other IEEE networks
Wireless devices
  Not designed to simultaneously transmit and receive
  Cannot prevent collisions
  Use different access method than Ethernet

## Slide 18: Access Method
CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)
  Minimizes collision potential
  Uses ACK packets to verify every transmission
    Requires more overhead than 802.3
    Real throughput less than theoretical maximum
RTS/CTS (Request to Send/Clear to Send) protocol
  Ensures packets not inhibited by other transmissions
  Efficient for large transmission packets
  Further decreases overall 802.11 efficiency
Notes: Access Method
CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)
  Minimizes collision potential
  Uses ACK packets to verify every transmission
    Requires more overhead than 802.3
    Real throughput less than theoretical maximum
RTS/CTS (Request to Send/Clear to Send) protocol
  Ensures packets not inhibited by other transmissions
  Efficient for large transmission packets
  Further decreases overall 802.11 efficiency

## Slide 19: Access Method
Notes: Access Method

## Slide 20: IEEE 802.11 Frames
Notes: IEEE 802.11 Frames

## Slide 21: Configuring Wireless Connectivity Devices
Each AP comes with an installation program on CD-ROM or DVD
  Guides through setup process
Variables set during installation
  Administrator password
  SSID
  Whether or not DHCP is used
  Whether or not the SSID is broadcast
  Security options
Notes: Configuring Wireless Connectivity Devices
Each AP comes with an installation program on CD-ROM or DVD
  Guides through setup process
Variables set during installation
  Administrator password
  SSID
  Whether or not DHCP is used
  Whether or not the SSID is broadcast
  Security options

## Slide 22: 802.11 Wireless Network Security
802.11 standard security
  None by default
  SSID: only item required
Authentication
  Process of comparing and matching a client’s credentials with the credentials in a database
MAC filtering
  Prevents the AP from authenticating any device whose MAC address is not listed
Encryption
  Use of an algorithm to scramble data
Notes: 802.11 Wireless Network Security
802.11 standard security
  None by default
  SSID: only item required
Authentication
  Process of comparing and matching a client’s credentials with the credentials in a database
MAC filtering
  Prevents the AP from authenticating any device whose MAC address is not listed
Encryption
  Use of an algorithm to scramble data

## Slide 23: WPA/WPA2 (Wi-Fi Protected Access)
WPA
  Dynamically assigns every transmission its own key
WPA2
  Replacement for WPA
  A stronger encryption protocol
Most secure communication is made possible by combining a RADIUS server with WPA/WPA2
  Known as WPA-Enterprise or WPA2-Enterprise
Notes: WPA/WPA2 (Wi-Fi Protected Access)
WPA
  Dynamically assigns every transmission its own key
WPA2
  Replacement for WPA
  A stronger encryption protocol
Most secure communication is made possible by combining a RADIUS server with WPA/WPA2
  Known as WPA-Enterprise or WPA2-Enterprise

## Slide 24: Security Threats to Wireless Networks
War driving
  A hacker searches for unprotected wireless networks by driving around with a laptop configured to receive and capture wireless data transmissions
War chalking
  Hackers draw symbols with chalk on the sidewalk or wall near a vulnerable AP
  To make it known to other hackers
Notes: Security Threats to Wireless Networks
War driving
  A hacker searches for unprotected wireless networks by driving around with a laptop configured to receive and capture wireless data transmissions
War chalking
  Hackers draw symbols with chalk on the sidewalk or wall near a vulnerable AP
  To make it known to other hackers

## Slide 25: Security Threats to Wireless Networks
Evil twin
  A rogue AP planted in a network’s geological area to pose as an authorized AP
WPA attacks
  Involve an interception of the network keys communicated between stations and APs
  Also called WPA cracking
WPS attack
  Cracking a PIN in order to access an APs settings
  Cracked through a brute force attack
Notes: Security Threats to Wireless Networks
Evil twin
  A rogue AP planted in a network’s geological area to pose as an authorized AP
WPA attacks
  Involve an interception of the network keys communicated between stations and APs
  Also called WPA cracking
WPS attack
  Cracking a PIN in order to access an APs settings
  Cracked through a brute force attack

## Slide 26: Avoiding Pitfalls
Wireless configuration pitfalls to avoid:
  SSID mismatch
  Incorrect encryption
  Incorrect or overlapping channels or frequencies
  Mismatched standards
  Incorrect antenna placement
  Interference
  Simultaneous wired and wireless connections
  Problems with firmware updates
  Unoptimized access point power levels
  Inappropriate antenna type
  Client saturation
Notes: Avoiding Pitfalls
Wireless configuration pitfalls to avoid:
  SSID mismatch
  Incorrect encryption
  Incorrect or overlapping channels or frequencies
  Mismatched standards
  Incorrect antenna placement
  Interference
  Simultaneous wired and wireless connections
  Problems with firmware updates

## Slide 27: Summary
Most wireless networks use frequencies around 2.4 GHz or 5 GHz
A signal may pass through an object, be absorbed by the object, or it may be subject to any of the following: reflection, diffraction, or scattering
Personal area networks (PANs) rarely exceed a few meters and usually only contain a few personal devices
Bluetooth technology unites mobile devices with PCs under a single communications standard
Notes: Summary
Most wireless networks use frequencies around 2.4 GHz or 5 GHz
A signal may pass through an object, be absorbed by the object, or it may be subject to any of the following: reflection, diffraction, or scattering
Personal area networks (PANs) rarely exceed a few meters and usually only contain a few personal devices
Bluetooth technology unites mobile devices with PCs under a single communications standard

## Slide 28: Summary
NFC is a form of radio communication that transfers data wirelessly over very short distances
The IEEE 802.11 task groups that have generated notable wireless standards are 802.11b, 802.11a, 802.11g, 802.11n, and 802.11ac
CSMA/CA minimized the potential for collisions but cannot detect the occurrence of a collision
Placement of an access point on a WLAN must take into account the typical distances between the access point and its clients
Notes: Summary
NFC is a form of radio communication that transfers data wirelessly over very short distances
The IEEE 802.11 task groups that have generated notable wireless standards are 802.11b, 802.11a, 802.11g, 802.11n, and 802.11ac
CSMA/CA minimized the potential for collisions but cannot detect the occurrence of a collision
Placement of an access point on a WLAN must take into account the typical distances between the access point and its clients

## Slide 29: Summary
If an access point is broadcasting its SSID clients in the vicinity will detect it
iwconfig is a command-line function for viewing and setting wireless interface parameters
By default the 802.11 standard does not offer any security
When configuring WEP, you establish a character string required to associate with the access point
WEP was replaced by WPA, which dynamically assigns every transmission its own key
Notes: Summary
If an access point is broadcasting its SSID clients in the vicinity will detect it
iwconfig is a command-line function for viewing and setting wireless interface parameters
By default the 802.11 standard does not offer any security
When configuring WEP, you establish a character string required to associate with the access point
WEP was replaced by WPA, which dynamically assigns every transmission its own key

## Slide 30: Summary
Wireless networks are susceptible to eavesdropping
Many programs exist that can scan for wireless signals over a certain geographical range
Wireless networks provide the best performance when the channels being used don’t overlap with those used by nearby networks
Notes: Summary
Wireless networks are susceptible to eavesdropping
Many programs exist that can scan for wireless signals over a certain geographical range
Wireless networks provide the best performance when the channels being used don’t overlap with those used by nearby networks